| Activity / Task: Working at Height on Ladders and Step Ladders |
| --- |
| Persons at Risk: Employees, Volunteers |
| Additional Information | HSE Guidance INDG403 – Safe use of Ladders and Stepladders HSE Guidance INDG – Top tips for Ladders and Stepladders Safety http://www.hse.gov.uk/pubns/indg455.htm |
| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| Injury due to: Falling from Height | Work at height risk assessment (this assessment) must be completed Ladders only to be used for short duration work and where no other type of platform is suitable. Ladders tied (by poles not rungs) and footed, at correct angle (75 degrees) where possible Ladders to be positioned on an appropriate surface Stepladders to be opened fully and lock into position Do not carry items up a ladder unless in a tool belt/bag Three points of contact to be maintained at all times Do not overstretch from a ladder Ladders to extend to a minimum of 1 metre above landing platforms Stepladders to be of suitable height to allow for work to be carried out. Users knees must not go above top step. Ensure that two persons are present and one used to foot the ladder. | Without Controls |  |
|  |  | 5 | 4 | 20 HIGH |  |
|  |  | With all controls in place: |  |
|  |  | 3 | 2 | 6 LOW |  |

| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| --- | --- | --- | --- | --- | --- |
| Injury due to: Falling Objects | Head protection must be issued and used Working area must be segregated from the public | Without Controls |  |
|  |  | 4 | 1 | 4 LOW |  |
|  |  | With all controls in place: |  |
|  |  | 3 | 2 | 6 LOW |  |

| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| --- | --- | --- | --- | --- | --- |
| Injury due to: Defective Equipment | Ladders checked prior to use Ladders used the right way up Do not paint ladders Defective ladders immediately removed from use and destroyed Do not use damaged ladders | Without Controls | 10 Medium |  |
|  |  | 5 | 2 |  |  |
|  |  | With All Controls in Place | 5 LOW |  |
|  |  | 5 | 1 |  |  |

| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| --- | --- | --- | --- | --- | --- |
| Injury due to: Ladders disturbed | Avoid placing ladders and stepladders where they may be struck by doors opening, persons passing, vehicles etc Cordon off the working area | Without Controls |  |
|  |  | 5 | 3 | 15 HIGH |  |
|  |  | With all controls in place: |  |
|  |  | 3 | 2 | 6 LOW |  |

| SEVERITY (CONSEQUENCE) |  | RISK / PRIORITY INICATOR MATRIX |
| --- | --- | --- |
| 1. Negligible (delay only) |  | LIKELIHOOD | 5 | 5 | 10 | 15 | 20 | 25 |
| 2. Slight (minor injury / damage / interruption) |  |  | 4 | 4 | 8 | 12 | 16 | 20 |
| 3. Moderate (Lost time injury, illness, damage, lost business) |  |  | 3 | 3 | 6 | 9 | 12 | 15 |
| 4. High (Major injury / damage, Lost time business interruption, disablement) |  |  | 2 | 2 | 4 | 6 | 8 | 10 |
| 5. Very High (Fatality / Business closure) |  |  | 1 | 1 | 2 | 3 | 4 | 5 |
|  |  |  | 1 | 2 | 3 | 4 | 5 |
| LIKELIHOOD |  |  | SEVERITY (CONSEQUENCE) |
| 1. Improbable / very unlikely |  |  |  |  |  |  |  |  |
| 2. Unlikely |  | SUMMARY | SUGGESTED TIMEFRAME |
| 3. Even chance / may happen |  | 12-25 | High | As soon as possible |
| 4. Likely |  | 6-11 | Medium | Within next 3-6 months |
| 5. Almost certain / imminent |  | 1-5 | Low | Whenever viable to do so |